Multi-instantiable and re-entrant safe driver

Modeled after TI Device Driver Architecture for Stream Class Devices that allows for easy porting and customization

Description

This EDMA3 Resource Manager has been developed for the following h/w and s/w environment

Hardware:

- Target Boards: DA830 EVM.

- Emulation Setup: TI Emulator

- Cabling: Standard Serial Connector

Software:

- CCS - 4.0.0.8.3

- Operating System: DSP BIOS – 6.10

- C6x Code generation tools: 6.1.5

- XDC Tool chain: 3.10.02

Other S/W Components Used:

- None

Capabilities

The DSP BIOS EDMA3 Resource Manager adopts a scalable architecture that eases customization/extension

- Isolates H/W and OS Accesses, Easy to maintain & re-target to new platforms

- Can stack custom-functions along control/data-path to realize “driver filters”

- Supports Multiple Instances

For easy and quick reconfiguration of driver for different SoCs, all its global configurable parameters can be passed at run time to the API EDMA3_DRV_create (), to create the SoC specific EDMA3 Driver Object. In case this configuration is not passed at run time, it can be taken from the EDMA3 configuration file edma3_<PLATFORM_NAME>_cfg.c, for the specific SoC, if it has been provided there. The configuration files can be found in “edma3_lld_<VERSION_NUMBER>\packages\ti\sdo\edma3\rm\src” folder.

Similarly, the shadow region specific information can also be passed at run time to the API EDMA3_DRV_open (), to create region specific EDMA3 Driver Instance. In case this configuration is not passed at run time, it can be taken from the EDMA3 configuration file edma3_<PLATFORM_NAME>_cfg.c, for the specific SoC, if it has been provided there. The configuration files can be found in “edma3_lld_<VERSION_NUMBER>\packages\ti\sdo\edma3\rm\src” folder.

EDMA3 Resource Manager APIs:

| EDMA3_RM_create () | Create (and initialize) a given EDMA3 Resource Manager (object) |
| --- | --- |
| EDMA3_RM_delete () | Delete a given EDMA3 Resource Manager (object) |
| EDMA3_RM_open () | Open instance of the EDMA3 Resource Manager |
| EDMA3_RM_close () | Close instance of the EDMA3 Resource Manager |
| EDMA3_RM_allocResource () | Request for a resource |
| EDMA3_RM_freeResource () | Free the earlier requested resource |
| EDMA3_RM_mapEdmaChannel () | Bind a DMA Channel to a PaRAM Set |
| EDMA3_RM_mapQdmaChannel () | Bind a QDMA Channel to a PaRAM Set and set the trigger word for the QDMA channel |
| EDMA3_RM_registerTccCb () | Register a callback against a TCC |
| EDMA3_RM_unregisterTccCb () | Unregister the callback from the TCC |
| EDMA3_RM_allocContiguousResource () | Allocate a contiguous region of specified resource |
| EDMA3_RM_freeContiguousResource () | Free a contiguous region of specified resource |
| EDMA3_RM_setCCRegister () | Set the Channel Controller (CC) Register value, by specifying the register offset and the new value. |
| EDMA3_RM_getCCRegister () | Get the Channel Controller (CC) Register value, by specifying the register offset. |
| EDMA3_RM_waitAndClearTcc () | Wait for a transfer completion interrupt to occur on the specific TCC. |
| EDMA3_RM_checkAndClearTcc () | Returns the status of a previously initiated transfer. |
| EDMA3_RM_allocLogicalChannel () | Request a DMA/QDMA/Link channel. |
| EDMA3_RM_freeLogicalChannel () | This API is used to free the specified channel (DMA/QDMA/Link) and its associated resources (PaRAM Set, TCC etc). |
| EDMA3_RM_setPaRAM () | Set the PaRAM Set associated with a logical channel |
| EDMA3_RM_getPaRAM () | Get the PaRAM Set associated with a logical channel |
| EDMA3_RM_getPaRAMPhyAddr () | Get the PaRAM Set Physical Address associated with a logical channel. |
| EDMA3_RM_getBaseAddress () | Get the Channel Controller or Transfer Controller (n) Physical Address. |
| EDMA3_RM_getGblConfigParams () | Get the SoC specific configuration structure for the EDMA3 Hardware. |
| EDMA3_RM_getInstanceInitCfg () | Get the Resource Manager Instance specific configuration structure for different EDMA3 resources' usage (owned resources, reserved resources etc). |
| EDMA3_RM_Ioctl () | This function provides IOCTL functionality for EDMA3 Resource Manager. |

Driver Performance Characteristics

| EDMA3 PRODUCT | PROGRAM MEMORY (in bytes) | data memory (in bytes) |
| --- | --- | --- |
|  |  | memory type | total |
|  |  | Initialized | Un Initialized |  |
| <EDMA3 Resource Manager> | 18240 | 1614 | 10266 | 30120 |

- EDMA3 Resource Manager Total Memory (Code & Data): 30120 Bytes

References

[1] EDMA3 Module Hardware Specifications

[2] DSP BIOS Documentation

[3] EDMA3 Resource Manager Documentation

Glossary

PaRAM Set	Parameter RAM Set in an EDMA3 Controller

# IMPORTANT NOTICE

Texas Instruments Incorporated and its subsidiaries (TI) reserve the right to make corrections, modifications, enhancements, improvements, and other changes to its products and services at any time and to discontinue any product or service without notice. Customers should obtain the latest relevant information before placing orders and should verify that such information is current and complete. All products are sold subject to TI's terms and conditions of sale supplied at the time of order acknowledgment.

TI warrants performance of its hardware products to the specifications applicable at the time of sale in accordance with TI's standard warranty. Testing and other quality control techniques are used to the extent TI deems necessary to support this warranty. Except where mandated by government requirements, testing of all parameters of each product is not necessarily performed.

TI assumes no liability for applications assistance or customer product design. Customers are responsible for their products and applications using TI components. To minimize the risks associated with customer products and applications, customers should provide adequate design and operating safeguards.

TI does not warrant or represent that any license, either express or implied, is granted under any TI patent right, copyright, mask work right, or other TI intellectual property right relating to any combination, machine, or process in which TI products or services are used. Information published by TI regarding third- party products or services does not constitute a license from TI to use such products or services or a warranty or endorsement thereof. Use of such information may require a license from a third party under the patents or other intellectual property of the third party, or a license from TI under the patents or other intellectual property of TI.

Reproduction of information in TI data books or data sheets is permissible only if reproduction is without alteration and is accompanied by all associated warranties, conditions, limitations, and notices. Reproduction of this information with alteration is an unfair and deceptive business practice. TI is not responsible or liable for such altered documentation.

Resale of TI products or services with statements different from or beyond the parameters stated by TI for that product or service voids all express and any implied warranties for the associated TI product or service and is an unfair and deceptive business practice. TI is not responsible or liable for any such statements.